## Slide 1: METAL SHOP SAFETY
IF YOU CAN’T BE SAFE, YOU CAN’T BE HERE

## Slide 2
THERE IS MACHINERY IN HERE THAT CAN
BREAK BONES
BADLY BURN YOU CUT OFF FINGERS

## Slide 3: BEHAVIOUR
NO HORSEPLAY
NO ROUGH-HOUSING
NO RUNNING

## Slide 4: BEHAVIOUR
NO UNNECESSARY NOISE
  We need to hear what’s going on
  Machines: “good” sounds and “bad” sounds
PAY ATTENTION TO OTHERS
  They might not pay attention to you

## Slide 5: ATTIRE
NO JEWELRY
  Rings, bracelets, necklaces,
  ties, etc.
NO LOOSE CLOTHING
  Hoodie strings, baggy clothes, earphones, etc

## Slide 6: ATTIRE
NO LONG HAIR
  Tie it back
WEAR NATURAL FIBER
CLOTHING
  Cotton, leather, etc.

## Slide 7: PROCEDURAL
WORK CLEAN & HELP CLEAN
  A clean shop is a safe shop
NO DISTRACTIONS
  Ear buds, daydreaming, under influence of…?

## Slide 8: PROCEDURAL
ASK FOR HELP or DEMOS
  I love the “teaching” part of my job
LOCKOUT or UNPLUG the machine when making adjustments
  No accidental “turn on”

## Slide 9: PROCEDURAL
STAND AN ARM’S LENGTH AWAY
  If the operator could punch you, you’re too close, give them room
KEEP FINGERS A HAND WIDTH’S AWAY FROM CUTTERS
  “No Finger Zone”

## Slide 10: SAFETY EQUIPMENT
THE #1 MOST IMPORTANT:
EYE PROTECTION
  Cutting, striking, shaping or
  removing metal

## Slide 11: SAFETY EQUIPMENT
HAND PROTECTION
  Risk of burns or cuts
  Don’t get them wet! (wrecks them)
  Don’t pick up hot metal! (wrecks them)
EAR PROTECTION
  Near loud noises
  If you have to raise your voice,
  you need ear protection

## Slide 12: TOOLS

## Slide 13: AVIATION SNIPS
For cutting SHEET METAL only! (it shears)
  Serrated teeth
  Green Cuts Left
  Yellow Cuts Straight
  Red Cuts Right

## Slide 14: SIDE CUTTERS
AKA “Diagonal Pliers”
For cutting ROUND material (it pinches)

## Slide 15: ADJUSTABLE WRENCH
Useful, but can RUIN nuts and bolts if not adjusted tightly
NOT a recommended tool

## Slide 16: VISE
For CLAMPING your project
JAWS will damage your project
  Use SOFT metal to protect YOUR project

## Slide 17: ANVIL
For SUPPORTING or SHAPING metal
  Best for Center-Punching

## Slide 18: BALL PEEN HAMMER
For SHAPING and STRIKING
WEAR EYE PROTECTION
  Hardened steel (DO NOT STRIKE TWO HAMMERS TOGETHER)

## Slide 19: CENTER PUNCH
For MARKING HOLES for drilling
  Use with a HAMMER (WEAR EYE PROTECTION)
  90° point

## Slide 20: CROSS PEEN HAMMER
WEAR EYE PROTECTION
Pointy end used to widen metal in Blacksmithing

## Slide 21: FOOT SHEAR
For cutting SHEET METAL ONLY
NO ROUND!!!

## Slide 22: JEWELRY SAW
EYE PROTECTION
BABY the blade
  Be VERY gentle!
Teeth point TOWARD the handle

## Slide 24: FILE
For SHAPING metal
EASILY dulled, chipped or broken!
  Be GENTLE!!!
  DO NOT bang together or against anything
  Works on PUSH stroke only

## Slide 25: HAND DRILL & DRILL PRESS
Makes holes
Wear EYE PROTECTION
All material must be CLAMPED DOWN

## Slide 26: HAND DRILL & DRILL PRESS
All holes must be CENTER-PUNCHED
  Wear EYE PROTECTION!
Any hole bigger than 1/4” must be PRE-DRILLED With a smaller drill bit

## Slide 27: BUFFING WHEEL
Wear EYE PROTECTION
Polish on BOTTOM of wheel
(Top spins towards you)
CAUTION: Polishing gets HOT!
NO CHAINS!

## Slide 28: LATHE

## Slide 29: LATHE
Makes things ROUND
Wear EYE PROTECTION
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning chuck
It WILL mess you up
Notes: Kid in Vernon. Lathe RIPPED his shirt off his body, and was pulling him in by the collar. His face was AT his work in SECONDS by the time the teacher got the power shut off.

## Slide 30
Notes: This raises more questions than it answers. 1) Why is he even touching the work? 2) Why does he have long sleeves? 3) Why is there a camera on this lathe? 4) If this is staged, dude has balls. 5) Look how fast this all happened – no time to react!

## Slide 31: LATHE
Be nice to the cutter – take BABY cuts
NEVER leave the CHUCK KEY in the CHUCK!!
Spin the chuck BY HAND before you turn it on!!

## Slide 32: LATHE
Cutter should be ~90° to direction of travel
Cutting tip should be same height as project center

## Slide 33: MILLING MACHINE
Makes things FLAT
Wear EYE PROTECTION

## Slide 34: MILLING MACHINE
Material MUST be WELL CLAMPED
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning cutter
  It WILL mess you up

## Slide 35: MILLING MACHINE
Cut AGAINST the rotation of the cutter
Be nice to the cutter – take light cuts (Chip Colour!)

## Slide 36: BELT SANDER
For finishing metal surfaces
EYE PROTECTION
Watch your fingers
Sand on DOWN side of disk rotation

## Slide 37: BLACKSMITH FORGE
HOT!
FACE SHIELD!
EAR PROTECTION!
LEATHER GLOVES!
BRAINS
  There’s a story behind that….
Notes: Grade 10 meathead of a kid heated up a stainless ruler in the forge and smacked on the back of the neck of a student, badly burning him. Kid chose not to press charges through the RCMP (against my recommendation). I kicked the offending kid of off my class and ALL my classes forever. I also “locked out” the forge and the entire class could no longer do blacksmithing for the rest of the year.