## Slide 1: METAL SHOP SAFETY
IF YOU CAN’T BE SAFE, YOU CAN’T BE HERE

## Slide 2
THERE IS MACHINERY IN HERE THAT CAN
BREAK BONES
AND
CUT OFF FINGERS

## Slide 3: BEHAVIOUR
NO HORSEPLAY
NO ROUGH-HOUSING
NO RUNNING
9

## Slide 4: BEHAVIOUR
NO UNNECESSARY NOISE
  We need to hear what’s going on
  Machines: “good” sounds and “bad” sounds
PAY ATTENTION TO OTHERS
  They might not pay attention to you
9

## Slide 5: ATTIRE
NO JEWELRY
  Rings, bracelets, necklaces,
  ties, etc.
NO LOOSE CLOTHING
  Hoodie strings, baggy clothes, earphones, etc
9

## Slide 6: ATTIRE
NO LONG HAIR
  Tie it back
WEAR NATURAL FIBER
CLOTHING
  Cotton, leather, etc.
9

## Slide 7: PROCEDURAL
WORK CLEAN & HELP CLEAN
  A clean shop is a safe shop
NO DISTRACTIONS
  iPod, daydreaming, under influence of…?
9

## Slide 8: PROCEDURAL
ASK FOR HELP or DEMOS
  I love the “teaching” part of my job
LOCKOUT or UNPLUG the machine when making adjustments
  No accidental “turn on”
9

## Slide 9: PROCEDURAL
STAND AN ARM’S LENGTH AWAY
  If the operator could punch you, you’re too close, give them room
KEEP FINGERS A HAND WIDTH’S AWAY FROM CUTTERS
  “No Finger Zone”
9

## Slide 10: SAFETY EQUIPMENT
THE #1 MOST IMPORTANT:
EYE PROTECTION
  Cutting, striking, shaping or
  removing metal
  Goggles: Minimum
  Face Shield: BEST
9

## Slide 11: YOU NEED EYE PROTECTION
…If it plugs in
…If it turns on
…If it removes material
BEST PRACTICE:
ALWAYS wear eye protection
9

## Slide 12: SAFETY EQUIPMENT
HAND PROTECTION
  PROTECT against burns or cuts
  DO NOT get them wet! (that wrecks them)
  DO NOT pick up hot metal! (that wrecks them)
9

## Slide 13
DO NOT PICK UP
HOT METAL
WITH GLOVES!
>USE PLIERS<

## Slide 14: SAFETY EQUIPMENT
EAR PROTECTION
  Near loud noises
  If you have to raise your voice,
  you need ear protection
9

## Slide 15: TOOLS

## Slide 16: RULER
Precision MEASURING instrument
For scribing STRAIGHT lines
Millimetres and Inches (KNOW the difference!)
9

## Slide 17: SCRIBER
For PRECISE MARKING of material
  SHARP 135° point
  Pencil & ink rub off
  FELT PEN is NOT accurate enough for metal.
9

## Slide 18: SQUARE
For marking or checking a SQUARE EDGE (90°)

## Slide 19: CENTER PUNCH
For MARKING HOLES for drilling
  Use with a HAMMER (wear eye protection)
  90° point
9

## Slide 20: AVIATION SNIPS
For cutting SHEET METAL only! (it shears)
  Serrated teeth
  Green Cuts Left
  Yellow Cuts Straight
  Red Cuts Right
9

## Slide 21: 45° BENT NOSE PLIERS
AWESOME for Art Metal and Jewelry
9

## Slide 22: MINI BOLT CUTTERS
AWESOME for cutting round!
9

## Slide 23: SIDE CUTTERS
AKA “Diagonal Pliers”
For cutting ROUND material (it pinches)

## Slide 24: SLIP JOINT PLIERS
AWESOME for picking up HOT and WELDED METAL! (Do not use gloves!!)
NOT for nuts and bolts!!!
Adjustable for two sizes of gripping
9

## Slide 25: LINEMAN’S PLIERS

## Slide 26: NEEDLE NOSE PLIERS

## Slide 27: MIG PLIERS (WELPERS)
AWESOME!
  Used with MIG Welder
  Grip
  Cut wire
  Clean nozzle

## Slide 28: WRENCH
AWESOME for NUTS and BOLTS
If possible, always use the BOX end

## Slide 29: ADJUSTABLE WRENCH
Useful, but can RUIN nuts and bolts if not adjusted tightly
NOT a recommended tool
9

## Slide 30: VISE
For CLAMPING your project
JAWS will damage your project
  Use SOFT metal to protect YOUR project
9

## Slide 31: ANVIL
For SUPPORTING or SHAPING metal
  Best for Center-Punching
9

## Slide 32: BALL PEEN HAMMER
For SHAPING and STRIKING
WEAR EYE PROTECTION
  Hardened steel (DO NOT STRIKE TWO HAMMERS TOGETHER)
9

## Slide 33: CROSS PEEN HAMMER
Used for striking and shaping
Pointy end used to widen metal in Blacksmithing
WEAR EYE PROTECTION
9

## Slide 34: BODY HAMMER
Very light weight
For flattening thin sheet metal
  Delicate hits
  Always support metal with a dolly
WEAR EYE PROTECTION
9

## Slide 35: FOOT SHEAR
For cutting SHEET METAL ONLY
NO ROUND!!!
9

## Slide 36: HAND SHEAR
For cutting SHEET METAL ONLY
Doesn’t do “curves” well
NO ROUND!!!
Notes: https://www.youtube.com/watch?v=eBbZK03MUVw

## Slide 37: THROATLESS SHEAR
For cutting SHEET METAL ONLY in curves
Doesn’t do “straight” well
NO ROUND!!!
Notes: https://www.youtube.com/watch?v=4mBtKpUwN9k

## Slide 38: HACKSAW
Cuts metal
Keep AT LEAST 3 teeth touching metal at all times
BABY the blade!
  CUT SLOW and use PRESSURE
  FAST = HEAT = DULL BLADE!
TEETH point away from the handle
9

## Slide 39: DON’T PUNCH THE VISE
“Listen” to the sound of the cut
  The pitch changes as you get closer to finishing
DO NOT punch the vise
9

## Slide 40: HACKSAW
A Hacksaw is a ONE-MAN tool
“How do I stop this from bleeding?”
9

## Slide 41: INTERMISSION
Hey: Mr. Wellwood: Do something else for a bit
- lots of love, Mr. Wellwood

## Slide 42: JEWELRY SAW
AWESOME for tiny, delicate cutting
BABY the blade!
  CUT SLOW and use PRESSURE
  FAST = HEAT = DULL BLADE!
TEETH point TOWARDS the handle
WEAR EYE PROTECTION
9

## Slide 43: FILE
For SHAPING metal
EASILY dulled, chipped or broken!
  Be GENTLE!!!
  DO NOT bang together or against anything
  Works on PUSH stroke only
9

## Slide 44: SLIP ROLLERS
For curving sheet metal ONLY
BABY the rollers
Make sure rollers are parallel or you will make a cone shape

## Slide 45: BEAD ROLLER
For rolling raised beads into sheet metal
For THIN sheet metal
Specific dies for specific purposes
Notes: https://www.youtube.com/watch?v=V4STgBsMam8

## Slide 46: HOSSFELD BENDER
AWESOME for bending
  Can bend just about anything
VERY cool machine

## Slide 47: FOR ALL POWER TOOLS
Stay at least AN ARM’S LENGTH AWAY from the operator!
Give them an “out” if something goes wrong

## Slide 48: HAND DRILL & DRILL PRESS
Makes holes
Wear EYE PROTECTION
All material must be CLAMPED DOWN
9

## Slide 49: HAND DRILL & DRILL PRESS
All holes must be CENTER-PUNCHED
Any hole bigger than 1/4” must be PRE-DRILLED With a smaller drill bit
9

## Slide 50
DEPTH STOP controls how DEEP you drill!
(Super handy)
9

## Slide 51: BENCH GRINDER
GRINDING – removes metal
Wear EYE PROTECTION
Wear EAR PROTECTION
For STEEL ONLY
  Check: magnet sticks to steel
  Non-steel metals (softer metals) PLUG the stone
  PLUGGED stones go not grind any more
  PLUGGED stones overheat and fail
  FAILED stones can injure you
9

## Slide 52: BENCH GRINDER
Tool Rest = 1/8” (3mm) away from stone
Stones may explode - Stand to one side when starting
Grind on the FACE of the stone only
9

## Slide 53: WIRE WHEEL
CLEANS metal
Wear EYE PROTECTION
Wire Wheel will SHRED your skin
https://www.youtube.com/watch?v=8jr-cE-l59k
9
Notes: https://www.youtube.com/watch?v=8jr-cE-l59k

## Slide 54: WIRE WHEEL
Wire wheel on the BOTTOM of the wheel
  Hold material tight enough that you have it, but loose enough that if the machine wants to eat your project, IT can have it.
NOT recommend to wear GLOVES
  There is a risk: gloves could get caught in the machine and cause a bigger accident
9

## Slide 55: BUFFING WHEEL
For ART METAL CLASS only
Wear EYE PROTECTION
Polish on BOTTOM of wheel
(Top spins towards you)
CAUTION: Polishing gets HOT!
NO CHAINS!
9

## Slide 56: ANGLE GRINDER
For grinding STEEL ONLY
Grind OUTSIDE
Watch where the sparks go
  Sparks hurt people
  Sparks ruin paint and glass
Wear EYE PROTECTION
Wear EAR PROTECTION
Wear GLOVES

## Slide 57: LATHE
9

## Slide 58: LATHE
Makes things ROUND
Wear EYE PROTECTION
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning chuck
It WILL mess you up
9
Notes: Kid in Vernon. Lathe RIPPED his shirt off his body, and was pulling him in by the collar. His face was AT his work in SECONDS by the time the teacher got the power shut off.

## Slide 59
9

## Slide 60: LATHE
NEVER leave the CHUCK KEY in the CHUCK
NEVER means NEVER
Spin the chuck BY HAND before you turn it on
9

## Slide 61: LATHE
Be nice to the cutter – take light cuts
  Watch chip colour:
  Gold is good
  Blue is bad
9

## Slide 62: LATHE
Cutter should be ~90° to direction of travel
Cutting tip should be same height as project center
9

## Slide 63: MILLING MACHINE
Makes things FLAT
Wear EYE PROTECTION
9

## Slide 64: MILLING MACHINE
Material MUST be WELL CLAMPED
Keep hands, arms, sleeves, hoodie strings THE HELL AWAY from the spinning cutter
  It WILL mess you up
9

## Slide 65: MILLING MACHINE
Cut AGAINST the rotation of the cutter
Be nice to the cutter – take light cuts (Chip Colour!)
9

## Slide 66: HORIZONTAL BANDSAW
For cutting reasonably to excessively thick metal
NO THIN METAL

## Slide 67: HORIZONTAL BANDSAW
At least 3 adjacent teeth in contact at ALL TIMES

## Slide 70: HOIZONTAL BANDSAW
Hold metal NO SHORTER THAN THE CLAMP

## Slide 71
Breaks Blade
SAVES BLADE

## Slide 72
< Hard on Teeth
EASY ON TEETH >

## Slide 73
< Hard on Teeth
Easy on Teeth >

## Slide 74: BLADE DEATH

## Slide 75: CHOP SAW
AWESOME for TUBING!
SUCKS at SOLID
EYE PROTECTION (FACE SHIELD)
EAR PROTECTION
CLAMP TIGHT
NO STEEP ANGLES!

## Slide 76: BELT SANDER
For finishing metal surfaces
EYE PROTECTION
Watch your fingers
Sand on DOWN side of disk rotation

## Slide 77: BLACKSMITH FORGE
HOT!
FACE SHIELD!
EAR PROTECTION!
LEATHER GLOVES!
LEATHER JACKET!
BRAINS!!
  There’s a story behind that….
9

## Slide 78
DO NOT PICK UP
HOT METAL
WITH GLOVES!
>USE TONGS<

## Slide 79
9