## Slide 1: TIG Welding

## Slide 2: WHAT TIG IS ABOUT
The most difficult to learn
Could be “the best” welding process (My Favourite!)
Pinpoint precision and heat control
Can weld:
  Aluminum (TIG is the best!)
  Steel
  Stainless Steel
  Magnesium
  Titanium
  _________
It can Braze & Bronze Weld

## Slide 3: WHAT TIG IS ABOUT
Electric ARC uses a Tungsten Electrode to melt the base metal
FILLER metal is added by hand
Weld bead is protected by an Inert shielding Gas

## Slide 4
https://www.youtube.com/watch?v=tNYmo2_DI6c

## Slide 5: CLEANLINESS & GROUNDS
TIG is STUPID FUSSY about CLEAN!
  Bare & shiny metal
  Use DEDICATED wire brush
  Wash in Acetone or Lacquer Thinner
A good ground is important
  Clamp the ground cable as close as you can to the weld
Surfacing disc, sandpaper, angle grinder, ground clamp.
Not shown: wire brush & acetone

## Slide 6: SHIELDING
Molten metal absorbs Oxygen = BAD
SHIELD the weld with an Inert Gas:
  “Inert” = “non-reacting”
  100% Argon
  About 18cfh
Shielding gas will continue to flow AFTER the welding is stopped
  About 1sec per 10amps
  Keep bead & filler shielded

## Slide 7: PARTS OF THE WELD

## Slide 8: PARTS OF THE TORCH

## Slide 9: SAFETY
Wear a full-face welding mask

## Slide 10: SKIN PROTECTION
Um….. I TIG in a long sleeve T-shirt. Shhhhh….
There are:
  No sparks
  No spatter
  No slag
  It’s very clean and quiet
Cover your skin!
15 minutes welding exposure = 10 hours sun exposure.

## Slide 11: LUNG PROTECTION
Well Ventilated Area
Welding Fumes have been known to cause:
  Cancer
  Birth Defects
  Lung damage
  Skin damage
  Eye Damage
  Bone/Joint damage
  Death
  http://www.ccohs.ca/oshanswers/safety_haz/welding/fumes.html

## Slide 12: SAFETY
NO LIGHTERS
  Lots of stories of explosion
  Lots of stories that this is false
  Let’s play it safe, and not become “that guy”

## Slide 13: ON/OFF & HEAT
“Heat” (current output) is fine-tuned by the user
Thumb button for on/off, and Thumb wheel for current
Foot pedal for both (I prefer this)
or

## Slide 14: YES, THAT MEANS:
One hand operates the torch
One hand operates the filler
One foot operates the pedal
Good luck!

## Slide 15: AMPERAGE
1 Amp per 0.001”
  10A for 0.010”
  63A for 0.063”
  125A for 0.125”
Steel & Stainless use DC CURRENT
Aluminum use AC CURRENT

## Slide 16: TUNGSTEN
Diameter selected by current
  1/16” (up to ~150 Amps)
  3/32” (150 to ~200 Amps)
  1/8” (200 to ~250 Amps)

## Slide 17: TUNGSTEN
Many different types
  Pure Tungsten
  2% Thoriated (Radioactive)
  2% Ceriated (we use this)
  1.5% Lanthanated
  Zirconiated
  ????
  (I’ve been using LaYzr:1.% Lanthanum, 0.08% Yttrium Oxides, 0.08% Zirconium)

## Slide 18: MAINTAIN THE ELECTRODE
The INSTANT you touch the tung the puddle or the rod, it’s contaminated!
STOP!
Grind vertical to the grinding wheel.
Tip length is 2-1/2 times the diameter

## Slide 19: FILLER ROD
Many different types, all identified by number
Common:
Aluminum = 4043
Steel = ER70S-2
Stainless = ER308
Carbon-Steel to Stainless Steel= ER309L

## Slide 20: TIG TIPS
Do a “dry run” to see if you can actually complete the full weld length in one go
Prop your hands on something
Filler rod should be applied 90° to tungsten
Watch the puddle “sink” into the metal before you add filler
No matter how slow you think you are going, go slower